## Slide 1: The Quake-Catcher Network: Visualization
J.F. Lawrence1, E.S. Cochran2, C.M. Christensen1,
A.I. Chung1, C. Neighbors2, J. Saltzman1
2University of California, Riverside
1Stanford University

## Slide 2: Primary Collaborators:
Birch Aquarium
California Academy of Science
Caltech
GNS (New Zealand)
IRIS
NEES
NSF
SCEC
Stanford
USGS
UC Berkeley
UC Los Angeles
UC Riverside
UC San Diego
U. Delaware
U. Concepcion (Chile)
U. de los Andes (Columbia)
UNAM (Mexico)
Additional Institutions:

## Slide 3: The Quake-Catcher Network
The Goal: Increase the number of seismic records of earthquakes to improve everyone’s understanding of earthquake science and earthquake hazards
Method: Combined Cyber-Social-Seismic Network
  Connect low-cost (<$150) MicroElectroMechanical Systems (MEMS) accelerometers to volunteer internet-connected computers

## Slide 4: QCN Seismic Sensors
MEMS Accelerometers:
  Free (Apple & Thinkpad laptops) or low cost ($30-150)
  Easy to install on Windows & Mac computers (based on BOINC software - NSF funded)
  Host computer provides power, shelter, & Internet (no maintenance costs)
  Specs:
    3 axes with ±2g dynamic range (1g=9.8m/s/s)
    Sensitivity between 4×10-2g & 2.4×10-8g ($30-$150)
  Useful for strong motion data collection
  Useful for education
    Real time demonstrations
    Participation in scientific discovery

## Slide 5: Download QCNLive
Download QCNLive
Uncompress the zip file.
Open the directory
Double click QCNLive
http://qcn.stanford.edu/downloads

## Slide 6: Install & Start QCNLive
Download QCNLive
Uncompress the zip file.
Open the directory
Double click QCNLive
http://qcn.stanford.edu/downloads

## Slide 7: Earthquake Viewing:
Circles:
  Blue: Historical
  Red: Recent
  Yellow: Currently selected
  Size increases with magnitude
Other:
  Pink: Plate boundaries
  Background: Topography
http://qcn.stanford.edu/downloads

## Slide 8: Earthquake Viewing:
Circles:
  Blue: Historical
  Red: Recent
  Yellow: Currently selected
  Size increases with magnitude
Other:
  Pink: Plate boundaries
  Background: Topography
http://qcn.stanford.edu/downloads

## Slide 9: Sensor Viewing: Real-time view
Download QCNLive
Uncompress the zip file.
Open the directory
Double click QCNLive
Provides an alternative to SeisMac (Cheaper to replace a sensor than a laptop or phone)

## Slide 10: Bouncing Cube:
Cube moves both left and right when you move the sensor sideways.
Difference between acceleration and displacement
http://qcn.stanford.edu/downloads

## Slide 11: Make a Quake: In collaboration with NEES
Select File & Make Earthquake
Enter Your Name
For K-12 demonstrations

## Slide 12: Make a Quake: In collaboration with NEES
Select File & Make Earthquake
For K-12 demonstrations
Fun way to get many students to interact: >400 in a day

## Slide 13: Make a Quake: In collaboration with NEES
Select File & Make Earthquake
For K-12 demonstrations
Fun way to get many students to interact: >400 in a day
Take home your own earthquake

## Slide 14
QCN’s Seismic Network
Participants
Earthquake Locations
Current Statistics
>1600 Seismic stations globally from >67 countries
Recorded earthquakes between M 2.5 – M 8.8
October 27, 2010

## Slide 15: Automatic Trigger & Data Upload
Automatically detect strong new signals:
  Maximize true (earthquake) triggers
  Minimize false (man-made) triggers
  Use efficient triggering algorithm for rapid reporting
Example 1: M 3.2 Earthquake in San Francisco Region

## Slide 16: Data Transfer Latency
Transfer minimal data including:
  Time
  Amplitude on each component
  Significance
  Station information (location, sensor type)
Low mean trigger latency
  3.62 seconds within California
  4.29 seconds globally
California
World

## Slide 17: Rapid Earthquake Detection

## Slide 18: Alert Maps: Expected Shaking Maps
Extrapolate current shaking to all other locations
Site effects seen from individual maximum amplitudes
Circles represent isocrons (equal-times) since/until the wave passes each location.
First maps in 7 seconds, later maps update features.
M6.0: February 22nd, 2011
14 sensors
Detected in 7 seconds
Updated until 25 seconds

## Slide 19: Scientific Objectives
Rapid earthquake detection:
  Rapid magnitude estimation
  Advanced Alert
Earthquake rupture
Ground motion amplification
Building monitoring

## Slide 20: Scientific Objectives
Rapid earthquake detection:
  Rapid magnitude estimation
  Advanced Alert
Earthquake rupture
Ground motion amplification
Building monitoring
www.scec.org

## Slide 21: Real Time Shaking:
Condense shaking to viewable format for 1000s of sensors.
Several seconds of latency.
http://qcn.stanford.edu/rt_image

## Slide 22: Scientific Objectives
Rapid earthquake detection:
  Rapid magnitude estimation
  Advanced Alert
Earthquake rupture
Ground motion amplification
Building monitoring
G. Prieto et al. 2009

## Slide 23: Scientific Objectives: Building Visualization
Courtesy of Debi Kilb
And Daniel Rohrlick

## Slide 24: Acknowledgements
Thanks to all of the QCN participants, especially K-12 teachers and classrooms
This project is supported in part by:
  National Science Foundation (NSF)
  Southern California Earthquake Center (SCEC)
  Incorporated Research Institutions for Seismology (IRIS)
  United Parcel Service (UPS)
More Information: http://qcn.stanford.edu

## Slide 25: For More Information:
Web Site: http://qcn.stanford.edu
Contact: Jesse F. Lawrence
Email: jflawrence@stanford.edu