## Slide 1: Understand Spectral Signature of Typical Landscape Materials Using in situ Spectroradiometer A lab in Remote Sensing and Image Interpretation Qian Yu, Dept. of Geosciences, University of Massachusetts-Amherst, qyu@geo.umass.edu
Objectives
To identify features based on spectral reflectance curves.
To determine the most useful bands for target discrimination.
Part 1. Measurement and Analysis of Target Reflectance
Each feature that we see has its own unique spectral reflectance curve (i.e. grass, water, gravel, etc). These curves are defined by the varying percent of reflectance. The color we see comes from the wavelengths which are reflected the most. Graphs of spectral reflectance curves help us better understand the reflectance nature of an object.
Spectroradiometer
In-situ or reference data is often collected at the time of image acquisition in the laboratory or in the field using a spectroradiometer, such as ASD Fieldspec. This device measures, as a function of wavelength, the energy coming from an object within its view. It is used primarily to prepare spectral reflectance curves for various objects.
Satellite image
Multispectral satellite sensors measure radiation in a series of discrete spectral bands (Landsat), while hyperspectral sensors measure over a continuous range (EO-1 Hyperion).
In this lab, you are to measure typical landscape objects using spectroradiometer and then plot the spectral reflectance curves in graphic format. The multispectral and hyperspectral bands can be simulated approximately by averaging spectroradiomenter reflectance for certain wavelength range. Again, plot the multispectral and hyperspectral reflectance curve. Comparing the plots will allow you understand the spectral resolution.
Part 2. Determining the Most Useful Bands for Target Discrimination
You are given an MS EXCELL table with the reflectance of three targets as a function of wavelength 350-2500 nm. These reflectance data were measured by spectroradiometer. Based on this data, calculate the average reflectance over blue, green, red and NIR ranges. Fill out the table below. You can assume this is the reflectance acquired by multi-band radiometer.
Spectral curve from ASD and multispectral bands from Landsat TM.
Chart: 
Wavelength (nm) | Bunker Ref | Grassland Ref | Deep Clear Water Ref
350 | 0.105 | 0.023 | 0.013
351 | 0.105 | 0.023 | 0.013
352 | 0.106 | 0.023 | 0.013
353 | 0.106 | 0.023 | 0.013
354 | 0.107 | 0.023 | 0.013
… | … | … | …
Read the table and spectral curves and determine which bands are most useful for target discrimination from experimental radiometric data. By analysis of experimental results such as these, the scientist may be able to choose the proper spectral band combinations for a given remote sensing task. Theoretically, the higher the reflectance contrast between any two imaged objects, the easier it should be to distinguish them. The easier an object is to distinguish, the greater the potential is for fast, accurate image interpretation.
In EXCEL, create a graph of spectroradiometer reflectance (y-axis) vs. wavelength (x-axis) and multi-band radiometer reflectance (y-axis) vs. wavelength (x-axis) respectively for each target. Y-axis uses the range 0-1. Use different colors to distinguish each of the individual target reflectance curves. Once you have completed the graph, answer the following questions:
In spectroradiometer reflectance curve, what do you observe at about 1.4 and 1.9 and 2.5 mm? why?
Determine which of the band available from muti-band radiometer is best for discriminating between the following target classes:
a. water and lawn
b. water and bunker
c. lawn and bunker
If you were to choose only two spectral bands to discriminate between all targets, which bands would you select and why?
Why do our eyes perceive healthy vegetation as green in color? What is the standard spectral reflectance curve for almost all healthy green vegetation?
How do you think the presence of moisture in soil will affect its reflectance?
 | B | G | R | NIR
λ (mm) range* |  |  |  | 
Water |  |  |  | 
Lawn |  |  |  | 
Bunker |  |  |  | 
* Use Landsat band ranges.